## Slide 1: Modern Optics
P47 – Optics: Unit 9

## Slide 2: Unit 9
Course Outline
Unit 1: Electromagnetic Waves
Unit 2: Interaction with Matter
Unit 3: Geometric Optics
Unit 4: Superposition of Waves
Unit 5: Polarization
Unit 6: Interference
Unit 7: Diffraction
Unit 8: Fourier Optics
Unit 9: Modern Optics

## Slide 3: Unit 9
Two Criteria for Laser Operation
Coherent amplification of an optical field
  Stimulated emission of radiation
  Population inversion in a 3 (or more) level system
Feedback from an optical cavity
  Fabry-Perot with partial reflector: Longitudinal modes
  Mirror curvature: Transverse modes and Gaussian beams
  Laser stability criteria, geometric optics, ABCD matrix.
LASER: Light Amplification by Stimulated Emission of Radiation

## Slide 4: Unit 9
Quantized Absorption & Emission
The quantum nature of light was first recognized in the context of absorption and emission by matter
  Photoelectric effect
    ejection of photoelectron by EM field
  Blackbody Radiation
    Stefan-Boltzmann
    Wien’s Law
    Planck Blackbody Spectrum

## Slide 5: Unit 9
A Collection of Two-Level Atoms
Have group of two level atoms (two energy levels)
  – the number of atoms in the ground state
  – the number of atoms in the excited state
  – the total number of atoms
Will consider a statistical mixture of populations ( in ; in )
What happens when we introduce photons (EM fields)?

## Slide 6: Unit 9
Optical Absorption
Atom is initially in the ground state
An incoming resonant photon is absorbed ()
Atom gets promoted to a higher energy state (e.g. raising an electron to a higher energy orbital)
If this is the only allowed process, what will happen to a collection of atoms illuminated continuously?
Energy Level Diagram

## Slide 7: Unit 9
Spontaneous Emission
If this is the only allowed process, what will happen to a collection of atoms initially in the excited state?
Energy Level Diagram
Atom is initially in the excited state
After some time, it will spontaneously decay to ground state
Upon decay, a resonant photon is emitted ()
This is called fluorescence

## Slide 8: Unit 9
Einstein Rate Equations
(No Driving Field)
Excited State:
Ground State:
Spontaneous emission () takes atoms from the excited state to the ground state at a rate
Any population in the excited state decays exponentially
( nanoseconds)

## Slide 9: Unit 9
Absorption Followed by Spontaneous Emission
Assumption: Atoms in the excited state will spontaneously decay into the ground state at some rate
Why? Vacuum fluctuations – a perturbation is necessary.
Energy Level Diagram
Momentum Space Diagram

## Slide 10: Unit 9
Einstein Rate Equations
(with Driving Field)
Excited State:
Ground State:
is the energy density of the electromagnetic field
(This picture is missing something very important)

## Slide 11: Unit 9
Absorption Followed by Stimulated Emission
This time, the rate that photons are emitted depends on the spectral energy density of the external field, .
Einstein realized that this must happen for the theory to be self-consistent
(ultimately what makes lasers possible…)
Energy Level Diagram
Momentum Space Diagram
identical

## Slide 12: Unit 9
Einstein Rate Equations
(with actual Driving Field)
Excited State:
Ground State:
is the energy density of the electromagnetic field ()
have now incorporated both stimulated emission and stimulated absorption terms

## Slide 13: Unit 9
Einstein Rate Equations
(Steady-State Case)
In steady-state, we have
Take rate equation for the exited state:
without stimulated emission, as
with stimulated emission, as , then
at most, half of atoms are excited
no gain/amplification… no laser.

## Slide 14: Unit 9
Einstein Rate Equations
(Coefficient Relations)
To get values for and requires knowledge of the specific atomic system and a quantum mechanical calculation…
BUT…
These are called the Einstein coefficients because he showed that there is an important connection between these three different coefficients, independent of the fine details.

## Slide 15: Unit 9
Einstein Rate Equations
(Coefficient Relations)
We’ll use specific information about the behavior of the two parts of this system in thermal equilibrium
1) Boltzmann: How much population must be in state 2 at temperature T ?
(population dependence eliminated!)

## Slide 16: Unit 9
Einstein Rate Equations
(Coefficient Relations)
We’ve eliminated dependence on population, now eliminate dependence on spectral power…
2) Planck Blackbody Spectral Energy Density:

## Slide 17: Unit 9
Einstein Rate Equations
(Strong Driving Limit)
no matter how big the driving field is!
Take-Home Point: It’s impossible to create a steady-state population inversion
    in a 2-level system!
If we can’t make a laser with this system….
what do we do now?
Add another level!

## Slide 18: Unit 9
Laser Pumping Schemes
(Three-Level Laser)
(fast)
(slow)
Assume we have a third level and some process that excites the atoms to that level at a rate
If the rate of spontaneous decay rate from is much faster than the decay rate from and the rate of pumping from , something very interesting becomes possible!

## Slide 19: Unit 9
Laser Pumping Schemes
(Population Inversion)
(fast)
(slow)
Adiabatic approximation for level 3!
This gives us an asymmetric way to get atoms into state 2 without having the pump interaction drive them right back down again at the same rate!
There’s almost no population in state 3 because it decays so fast

## Slide 20: Unit 9
Laser Pumping Schemes
(Population Inversion)
Again, look at the steady-state:
If we can make bigger than we can now create a population inversion and make a laser!

## Slide 21: Unit 9
Maiman’s Original Ruby Laser
(3-Level Pulsed Laser)
Theodore Harold "Ted" Maiman (July 11, 1927 – May 5, 2007)

## Slide 22: Unit 9
Helium-Neon (HeNe) Laser
(4-Level Continuous Wave Laser)
High voltage on electrodes creates a plasma
Electron collisions pump helium into several excited states (s)
Helium collides with neon and transfers its energy
With sufficient pumping, a population inversion of the metastable s state can occur

## Slide 23: Unit 9
Why would there be an advantage to this kind of setup?
(fast)
(slow)
(fast)

## Slide 24: Unit 9
Even if you screw-up engineering details of the laser,
at least you’ve fabricated a neon lamp

## Slide 25: Unit 9
Feedback and Laser Oscillation
Reflect some of the photons emitted from the gain medium back into it, where they can be amplified!
But not just any mirror configuration will do…

## Slide 26: Unit 9
Cavity Longitudinal Modes
(Fabry-Perot Laser Cavity)
For L=20 cm:
MHz
For L 20.0 cm and 632.8 nm:
The cavity length must be an integer number of half-wavelengths of the light
The laser can only operate at select frequencies separated by the cavity Free Spectral Range (FSR)

## Slide 27: Unit 9
Cavity Longitudinal Modes
Lasing depends on overlap of the gain profile with the cavity modes
Low-power (3 mW) cavity
L = 20 cm
FSR = 750 MHz
Lasing occurs on only 2 modes
Higher-power (30 mW) cavity
L = 80 cm
FSR = 186 MHz
Lasing occurs on 10 modes

## Slide 28: Unit 9
Cavity Transverse Modes
The mirrors are finite-sized…
Need solutions of the paraxial Helmholtz equation that vanish as becomes large
The simplest solution that we might use is the
Gaussian or electromagnetic field mode
The simplest solution we might consider is a
Gaussian Beam Mode:
Radial profile

## Slide 29: Unit 9
Higher-Order Transverse Modes
Laguerre-Gaussian Modes
Hermite-Gaussian Modes
(Cartesian – Laguerre polynomial basis)
(Cylindrical – Hermite Polynomial Basis)
Each one of these is its own Fourier transform!

## Slide 30: Unit 9
Transverse Cavity Stability
(will a photon stay inside?)
What affects whether a photon returns to the gain medium?
mirror separation
mirror curvatures and
mirror diameter
How can we quantify this?
Geometric optics…
Cavity stability analysis
A flat mirror cavity is unstable
(Why?)

## Slide 31: Unit 9
Cavity Stability: The ABCD Matrix
Propagation a distance d
(index of refraction = 1)
Curved spherical optic
(mirror or lens)
Can model the optical cavity by chaining these together

## Slide 32: Unit 9
ABCD Matrix of Optical Cavity
=
=
=
After some algebra…..
This tells us exactly how the ray will be transformed after one round trip in the cavity!

## Slide 33: Unit 9
Cavity Stability Criterion
The cavity will be stable if after many round trips the ray does not run off to infinity!
There is a straightforward formula for raising a 2x2 matrix to an arbitrary power:
Where
We need this expression to remain finite, given our cavity ABCD matrix
This implies that the ray will stay a finite distance from the cavity axis

## Slide 34: Unit 9
Cavity Stability Criterion
Point #1: N only appears within arguments of the sine function,
which is bounded by [-1,1]
Point #2: The only problem we will run into is if becomes imaginary
As long as
, will be real-valued, and the cavity is stable!
Where

## Slide 35: Unit 9
Cavity Stability Criterion
For our cavity earlier:
This gives us the criterion that
So, our L = 20 cm HeNe is stable for:
R

## Slide 36: Unit 9
Laser Summary
Einstein Coefficients
  A: spontaneous emission
  B: stimulated absorption/emission
Lasers require population inversion to work
Can’t invert a 2-level system (in steady-state)
3 and 4 level systems make population inversion possible
Need a stable cavity to enable feedback and laser oscillation

## Slide 37: Unit 9
http://www.physik.uni-r.de/forschung/lupton/lupton/

## Slide 38: Unit 9
http://www.physik.uni-r.de/forschung/lupton/lupton/

## Slide 39: Unit 9
Immanual Bloch Lab @ Max Planck Institute of Quantum Optics

## Slide 40: Unit 9
Current Optics Challenges Sampler Pack
JWST Launch 2019
Fuel energy gain in 2014,
break-even ???
Advanced LIGO
10 nm EUV lithography!

## Slide 41: Unit 9
Current Optics Challenges Sampler Pack
There are still plenty of epic optics challenges out there